----------104F00-----------------------------
INT 10 - VESA SuperVGA BIOS - GET SuperVGA INFORMATION
        AX = 4F00h
        ES:DI -> 256-byte buffer for SuperVGA information (see below)
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
SeeAlso: AX=4F01h

Format of SuperVGA information:
Offset  Size      Description
 00h   4 BYTEs    signature ('VESA')
 04h    WORD      VESA version number
 06h    DWORD     pointer to OEM name
 0Ah   4 BYTEs    capabilities
 0Eh    DWORD     pointer to list of supported VESA and OEM video modes
 12h   238 BYTEs  reserved
----------104F01-----------------------------
INT 10 - VESA SuperVGA BIOS - GET SuperVGA MODE INFORMATION
        AX = 4F01h
        CX = SuperVGA video mode
        ES:DI -> 256-byte buffer mode information (see below)
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
SeeAlso: AX=4F00h,AX=4F02h

Format of mode information:
Offset Size   Description
 00h   WORD   mode attributes
              bit 0: mode supported
              bit 1: optional information available
              bit 2: BIOS output supported
              bit 3: set if color, clear if monochrome
              bit 4: set if graphics mode, clear if text mode
 02h   BYTE   window A attributes
              bit 0: exists
              bit 1: readable
              bit 2: writable
              bits 3-7 reserved
 03h   BYTE   window B attributes (as for window A)
 04h   WORD   window granularity in K
 06h   WORD   window size in K
 08h   WORD   start segment of window A
 0Ah   WORD   start segment of window B
 0Ch   DWORD -> FAR window positioning function (equivalent to AX=4F05h)
 10h   WORD   bytes per scan line
---remainder is optional for VESA modes, needed for OEM modes---
 12h   WORD   width in pixels
 14h   WORD   height in pixels
 16h   BYTE   width of character cell in pixels
 17h   BYTE   height if character cell in pixels
 18h   BYTE   number of memory planes
 19h   BYTE   number of bits per pixel
 1Ah   BYTE   number of banks
 1Bh   BYTE   memory model type
 1Ch   BYTE   size of bank in K
----------104F02-----------------------------
INT 10 - VESA SuperVGA BIOS - SET SuperVGA VIDEO MODE
        AX = 4F02h
        BX = mode
             bit 15 set means don't clear video memory
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
SeeAlso: AX=4F01h,AX=4F03h

Values for VESA video mode:
  00h-FFh OEM video modes (see AH=00h)
 100h 640x400x256
 101h 640x480x256
 102h 800x600x16
 103h 800x600x256
 104h 1024x768x16
 105h 1024x768x256
 106h 1280x1024x16
 107h 1280x1024x256
 108h 80x60 text
 109h 132x25 text
 10Ah 132x43 text
 10Bh 132x50 text
 10Ch 132x60 text
----------104F03-----------------------------
INT 10 - VESA SuperVGA BIOS - GET CURRENT VIDEO MODE
        AX = 4F03h
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
        BX = video mode (see AX=4F02h)
SeeAlso: AX=4F02h
----------104F04-----------------------------
INT 10 - VESA SuperVGA BIOS - SAVE/RESTORE SuperVGA VIDEO STATE
        AX = 4F04h
        DL = subfunction
             00h get state buffer size
                 Return: BX = number of 64-byte blocks needed
             01h save video states
                 ES:BX -> buffer
             02h restore video states
                 ES:BX -> buffer
                 CX = flags for states to save/restore
                      bit 0: video hardware state
                      bit 1: video BIOS data state
                      bit 2: video DAC state
                      bit 3: SuperVGA state
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
----------104F05-----------------------------
INT 10 - VESA SuperVGA BIOS - CPU VIDEO MEMORY CONTROL
        AX = 4F05h
        BH = subfunction
             00h select video memory window
                 DX = window address in video memory (in granularity units)
             01h get video memory window
                 Return: DX = window address in video memory (in gran. units)
        BL = window number
             00h window A
             01h window B
Return: AL = 4Fh function supported
        AH = status
             00h successful
             01h failed
SeeAlso: AX=4F06h,AX=4F07h,AX=7000h/BX=0004h
----------104F06-----------------------------
INT 10 - VESA SuperVGA BIOS 1.1 - GET/SET LOGICAL SCAN LINE LENGTH
        AX = 4F06h
        BL = function
             00h set scan line length
                 CX = desired width in pixels
             01h get scan line length
Return: AL = 4Fh if function supported
        AH = status
             00h successful
             01h failed
        BX = bytes per scan line
        CX = number of pixels per scan line
        DX = maximum number of scan lines
Notes: 	if the desired width is not achievable, the next larger width will be set
       the scan line may be wider than the visible area of the screen
       this function is valid in text modes, provided that values are
       multiplied by the character cell width/height
SeeAlso: AX=4F01h,AX=4F05h,AX=4F07h
----------104F07BH00-------------------------
INT 10 - VESA SuperVGA BIOS 1.1 - GET/SET DISPLAY START
        AX = 4F07h
        BH = 00h (reserved)
        BL = 00h set display start
                 CX = leftmost displayed pixel in scan line
                 DX = first displayed scan line
           = 01h get display start
                 Return: BH = 00h
                         CX = leftmost displayed pixel in scan line
                         DX = first displayed scan line
Return: AL = 4Fh if function supported
        AH = status
             00h successful
             01h failed
Note: this function is valid in text modes, provided that values are
      multiplied by the character cell width/height
SeeAlso: AX=4F01h,AX=4F05h,AX=4F06h
----------104FFF-----------------------------
INT 10 - VESA SuperVGA BIOS - Everex - TURN VESA ON/OFF
        AX = 4FFFh
        DL = new state (00h off, 01h on)